## Slide 1: Getting Started with Sint & Piet
Status as per 4 April 2012

## Slide 2: Elements of NDPF Service Cluster
GSP Piet “MTDR24”: 16 blade servers
Sint SAN storage “MTDR23”:50 TByte
Existing set of Generics 2008/A
  few of these will become a security VM cluster
  1-2 others become test systems
Existing blades “bl0”
  1-5, 13,14 will be upgraded to dual FC SAN
  10G stacked switches replace pass-through (Thu.)
Installnet switch (still now: deelmlx)
  Seperate installation network ve11 @1+10G
  IPMI management LAN ve4 for managementonly

## Slide 3: Storage
Dell Compellent Storage Center (6.0.3)
  sint.ipmi.nikhef.nl collective management
  username: Admin
78 TByte gross capacity
  auto-tiering ESSD, 10kRPMSAS, 7k2RPM N/L-SAS
  Default RAID 6-6 on Tier 2&3
  Default RAID-10 and 5-5 on Tier 1
  Effective capacity ~ 50 TByte

## Slide 4: Auto-tiering effect on used storage

## Slide 6: Caveats
Tier migration only works on replay volumes
  If you do not configure replay, data stays in primary storage most, usually on Tier-1
Choose a ‘custom’ template for all volumes
  for most volumes ‘Custom Sint’ is OK
  databases and high-IOPS: ‘Custom Sint Tier 1+2 HS’

## Slide 7: LUNs for VM hosting
You can (and should) host more than one VM system disk on a LUN
  But not too many since performance (IO queues) are per-LUN
  Allocation is sparse, so ‘0’s take no space
  On re-writing old VM images, space is not reclaimed
Put transient VMs in a dedicated pool LUN
  LUN can be removed after completion
Guideline: 10-15 VMs per LUN
Separate LUNs for Data, databases and $HOME

## Slide 8: Assigning LUNs to hosts
Xen clusters are Server Clusters which share use of each LUN
  this ‘server cluster’ must be defined as such on the Compellent, or Sint will warn for inconsistencies
  XCP/XenServer “Piet” with the dual FC paths uses EL5/Xen5.x multi-path “MP” IO
  Generics 2008/A iSCSI only has a single path, so uses XenServer 5.x IO
You cannot attach LUNs to a single server in a XCP cluster
You cannot share LUNs without using LVM

## Slide 9: Linking storage and compute
We have a dual-redundant FC mash-up
Key FC concepts:
  “WWN”: world-wide name, identifies an FC end-point or port on a FC card
  “zone”: a group of server end-points that can see eachother
  ‘soft zoning’: a zone based on WWNs
  ‘hard zoning’: zone based on physical ports
  “alias”: a friendly name for a WWN
  license: everything is licensed!
FC: switches v.s. ‘access gateways’

## Slide 11: Staf and Schimmel
Brocase SAN switches containing zone def
  two independent switches for each path
  cross-connect to the Compellent
  server ports (and AGw’s) connect to one of them, and servers have two FC ports for MPIO
  effectively, each host sees a LUN 4 times
Zones:
  Z_Sint_Piet01: contains both “Sint”s and all Piet’s
  Z_Sint_R710: contains both “Sint”s and Achtbaan

## Slide 12: Useful commands
alicreate "aliName","member[; member...]“
  name aliases after hostname and switch fabric
  alicreate “A_Piet03_C1” “20:01:24:b6:fd:be:23:e3” on switch staf.ipmi.nikhef.nl
zoneadd "zoneName", "member[; member]“
  add named aliases (please!) to a zone
  zoneadd “Z_Sint_Piet01”, “A_Piet03_C1; A_Piet_04_C1” on switch staf
on schimmel it would look like
  zoneadd “Z_Sint_Piet01”, “A_Piet03_C2”

## Slide 13: FC Configurations
changes in the CLI are the defined configuration, not yet the effective configuration settings
Save the configured settings
  cfgsave
Enable the configured settings
  cfgenable “C_Staf”
There can be multiple configuration, but for the time being that would just be confusing
Note that a single WWN can be a member of many zones

## Slide 14: iSCSI – for Generics and more

## Slide 15: GSP Piet
16 M610 blades,
  96 GByte RAM, 2x600 GB SAS disk in RAID-1 config
  2x6 cores with HT
  eth0+1: 1 Gbps, switch fabric A
  eth2+3: 10 Gbps, switch fabric B
  dual FC: 8 Gbps, switch fabric C
Enclosure: piet-blade.ipmi.nikhef.nl
Switches: sw-piet-<fabric><1|2>.ipmi.nikhef.nl
Blade DRAC: piet-<01..16>.ipmi.nikhef.nl

## Slide 16: Recommended BIOS
CPU: virtualisation enabled 
no memory checking on boot
boot order: disk, <rest>
To install
  mount the virtual CD-ROM via DRAC, via Java applet or ActiveX control
  press F11 during boot
  select ‘Virtual CD-ROM’
  Proceed with installation

## Slide 17: Ethernet Networking Piet

## Slide 18: Installation
Follow install guidance XCP1.5beta (1.4.90)
Hostnames
  vms-piet-XX.inst.ipmi.nikhef.nl, vms-gen-XX.inst....
Cluster master (via CNAME)
  pool-piet.inst.ipmi.nikhef.nl CNAME vms-piet-16...
static IP address (see Wiki or DNS)
  dedicated installnet “ve11” 172.22.64.0/18
  untagged over eth2 (eth0 for Generics 2008/A)
DNS: boer, stal, dwalin
NTP: stal, salado.inst (172.22.64.2), dwalin

## Slide 19: XenServer
XCP 1.5 looks like XenServer 6 w/o HA,WBS
Local configuration resembles CentOS5
Installed via CD-ROM
  Install image ISO on stal, or download from xen.org
  to make it look like XenServer, follow Wiki tweaks
Fit in local ‘GridSRV’-like management system
  run xcp-config.sh post-install script
  installs ssh keys of nDPFPrivilegedUsers for root
  configure bridged networking & txqueue performance
  https://wiki.nikhef.nl/grid/GSP_Virtualisation_with_Xen

## Slide 20: Pool Constraints
All hosts in the pool must have
  the same network configuration (devices, vlans)
  the same FC configuration for MPIO
  be in the same server pool on Sint
You can’t
  copy VDIs between SRs on different pools
  migrate VMs between pools
  mount the same storage r/w on different pools
  copy VDIs with the GUI (but you can with a CLI)

## Slide 21: XenCenter
Works best under Windows (sorry)
  CLI anyway needed for advanced configuration
  The CLI command is xe (see also: xe help --all)
Configuration
  connect to pool-piet.inst.ipmi.nikhef.nl, username: root
Caveats:
  no HA, so failing hardware will kill VMs
  Live migration: right-click to move VMs
  Maintenance mode: automatically moves VMs
  Maintenance on pool master: trigger alternate master (and remember to update DNS CNAME please)

## Slide 23: AII VM provisioning
Configure a machine with quattor
  make sure the hardware spec is really what you want
  compile the profile (the new biggerish-XML works)
  aii-shellfe --configure <hostname>
  aii-provision-vm --n “<hostname”> -a
After install: fixup XenTools version as per Wiki
network configuration is in .xapirc of ndpfmgr
stal:~:1030$ aii-provision-vm -n "boslook.nikhef.nl" -a
Parsing XML data from CDB, please wait ... Done.
Password:
Connecting to https://pool-piet.inst.ipmi.nikhef.nl/ as root ...
Creating new VM boslook.nikhef.nl on pool.
SR will be Public (Grid) VM Images low-IOPS series 1
Template used OpaqueRef:94142f41-6744-76da-881c-45570ae1938d
OS Repository http://stal.nikhef.nl/centos/5.7/os/x86_64/
Autoboot set to 1
Start on ready set to no
Creating NIC eth0 in Public Grid (194.171.97.0)

## Slide 24: Non-AII
Create host from template (“New VM”)
the install URL is like http://spiegel.nikhef.nl/mirror/centos/6/os/x86_64
boot options: ks=<url> graphical utf8
When the install fails first time
login to pool master
reset the boot loader to “eliloader”

## Slide 25: Tuning the VM and more
Memory balooning can be set through the GUI
  only after VM tools are installed
  and fixed to proper version
Live migration
  again easiest from GUI
  only within a pool
  only to same hardware
Across pools?
  you cannot live migrate across pools
  you cannot sanely share LUNs across pools

## Slide 26: About disks and images
VM disk images are stored in Storage Repositories
One LUN contains one SR
One SR can contain many disk images
An SR is always LVM volume, even on local disk
The default XCP disk image type is now VHD inside LVs, no longer raw LVM volumes
  in you copy in disk images, create the VDI yourself with type RAW
  when copying VDIs between SRs, they become VHD
  you cannot copy out VHDs to raw LVs

## Slide 27: Finding your SR
An SR is hosted on a LUN and reached via
  a local HBA for FC connected systems
  an iSCSI HBA for Generics 2008/A
  On FC, your LUN is visible immediately once you add the server to the server group on Sint
  On iSCSI, you need to trigger a discover on both sides at the same time (<30sec)
Provision the LUN on the Compellent first
For aii-provision-vm: making the desired SR the default SR eases creation of new VMs

## Slide 28: Import existing VM from EL5
Create a RAW LVM xe vdi-create \ sm-config:type=raw sr-uuid={SR_UUID} \ name-label="My Raw LVM VDI" \ virtual-size={size}GiB type=user
mount this LVM in the Dom0
  a lot safer than tweaking with lvchange –ay!
  vbd-create and vbd-plug
Copy the contents into it (may take a while!)
  you can try it with a live VM if the FS is stable
unplug please VDI from the dom0 VBD
  destroy the left-over vbd in the dom0
create a VM which boots pygrub (not eliloader)

## Slide 29: Backups and restore
SRs can be detaches and attached without trouble
DO NOT FORMAT AN SR if you think there’s useful data on it
Attach an SR only to one pool in RW mode

## Slide 30: Oops
If all is hosed recover from database dump (wiki!)
Or, if worst comes to worst:
  detach all SRs
  wipe all VM hosts (“enter maintenance mode” -> “remove server from pool”, or reinstall
  create a new pool
  re-attach the SRs, but do not format
  create a bootable template
  create VMs based on existing VDI disk images

## Slide 31: En Nu Zelf ...