## Slide 1: Nikhef – Advanced Computing for Research
Beyond just LHC Computing

## Slide 2
A global e-Infrastructure WLCG, federation, and collaboration
Systems for Science: inherently coherent management in multi-domain diverse infrastructures
Data transfers via LHCOPN and LHCone L3VPN and the Science DMZ
Building a data intensive data centre – without breaking the bank
DIY SDN: managing LHCOPN switching policies in the network layer
Interconnect, at least 100G please …
Federated cloud bursting – at L7 and L2, be it Paas-over-IaaS or just IaaS.

## Slide 3
Signal/Background 10-9
Data volume
  (high rate) X (large number of channels) X (4 experiments)
   20 PetaBytes of new data each year
Compute power
  (event complexity) X (number of events) X (thousands of users)
   60’000 of (today's) fastest CPUs
Concorde
(15 Km)
Balloon
(30 Km)
CD stack with
1 year LHC data!
(~ 20 Km)
Mt. Blanc
(4.8 Km)
Data from the LHC

## Slide 4: Today – LHC Collaboration
~ 5 000 physicists
~ 150 institutes
53 countries, economic regions
20+ years est. life span 24/7 global operations ~ 5000 person-years of science software investment

## Slide 5: The global e-Infrastructure

## Slide 6: BiG Grid, the Dutch e-Science Grid
Started @Nikhef in 1999 Nikhef with WTCW VL
  2001: European DataGrid and EGEE projects joint with SARA (and KNMI)
Started BiG Grid in 2005/2007 to consolidate e-Science infrastructure & production support
Initiative lead by the science domains
  NCF and its scientific user base
  NBIC, Netherlands BioInformatics Center
  Nikhef, where you are now
With SARA as main operational partner
    Resulting in SURF today coordinating the national e-Infra

## Slide 7: LCG Services
Tier-0 – the accelerator centre
Data acquisition & initial processing
Long-term data curation
Distribution of data  Tier-1 centres
Canada – Triumf (Vancouver)
France – IN2P3 (Lyon)
Germany – Forschunszentrum Karlsruhe
Italy – CNAF (Bologna)
Netherlands – NIKHEF/SARA (Amsterdam)
Nordic countries – distributed Tier-1
Spain – PIC (Barcelona)
Taiwan – Academia SInica (Taipei)
UK – CLRC (Oxford)
US – FermiLab (Illinois)
– Brookhaven (NY)
Tier-1 – “online” to the data acquisition process  high availability
Managed Mass Storage –  grid-enabled data service
Data-heavy analysis
National, regional support
Tier-2 – ~120 centres in ~35 countries
End-user (physicist, research group) analysis – where the discoveries are made
Simulation

## Slide 8
IN2P3
GridKa
TRIUMF
ASCC
Fermilab
Brookhaven
Nordic
CNAF
Nikhef SARA
PIC
RAL
T2
T2
T2
T2
T2
T2
T2
T2
T2
T2
T2
Tier-2s and Tier-1s are
inter-connected by the general purpose
research networks
Dedicated 10-40 Gbit
optical network
T2
Any Tier-2 may
access data at
any Tier-1
T2
T2
T2
LCG
Wide Area Network

## Slide 9: e-Science and National e-Infrastructure
Avian Alert and FlySafe
Willem Bouten et al.
UvA Institute for Biodiversity Ecosystem Dynamics, IBED
Data integration for genomics, proteomics, etc. analysis
Timo Breit et al.
Swammerdam Institute of Life Sciences
Medical Imaging and fMRI
Silvia Olabarriaga et al.
AMC and UvA IvI
Molecular Cell Biology and 3D Electron Microscopy
Bram Koster et al.
LUMC Microscopic Imaging group
Image sources: VL-e Consortium Partners

## Slide 10: Many user communities
HTC Grid Computing service

## Slide 11: Global collaboration (in a secure way)
Why would I trust you? How do I know who you are?
A global identity federation for e-Infra and cyberinfrastructures
Common baseline assurance requirements
Persistent and globally unique
For the Grid a truly global identity is needed –– so we built the International Grid Trust Federation
  over 80 member Authorities
  Including, e.g., the TCS
And it works in a global federation, with harmonized requirements, driven by actual relying parties

## Slide 12: R&E federations – providing multi-domain services
Multiple technologies (SAML2, OIDC, PKIX) allow cross-organisational ‘single sign-on’ – and trust between user home organisations and service providers created a global service ecosystem
Graphic courtesy Alessandra Sciccitano, GEANT
Notes: eduGAIN aggregates metadata from participating federations (metadata service). This aggregate is consumed by all participating federations, such that Identity Providers and Service Providers can find each other.
Technically, this aggregate works as follows:
Each participating federation produces a so called 'export metadata aggregate'; a file that contains the metadata of local Identity Providers and Service Providers that participate in eduGAIN. Note that this is often a subset of all Identity Providers and Service Providers from that federation.
eduGAIN combines all export metadata aggregates and generates an "eduGAIN aggregate"; a file that combines all metadata from all participating federations.
This eduGAIN aggregate is signed by eduGAIN and published on the internet, thereby making it available to all participating federations.
Each participating federation must consume this eduGAIN aggregate and supply it to their local Identity Providers and Service Providers. A federation can decide to filter out certain entities before making it available locally, e.g. filter out it's own entities, to prevent them from appearing in the metadata twice.

## Slide 13: And now we have this!
wLCG FIM4R pilot

## Slide 14: Systems for Science

## Slide 15: Statistics
Dutch National e-Infrastructure coordinated by
“BiG Grid” HTC and storage platform services
3 core operational sites: SURFsara, Nikhef, RUG-CIT
25+ PiB tape, 10+ PiB disk, 12000+ CPU cores
@Nikhef
~ 5500 cores and 3.5 PiB
~ 400 systems installs (focus on large/many-core systems)
> 45 install flavours (service types)
and a bunch of one-off systems

## Slide 16: For (informed) fun & testing – some random one-off systems …
CO2-cooled Intel CPUs @6.2GHz

## Slide 17: For (informed) fun & testing – some random one-off systems …
plofkip.nikhef.nl

## Slide 18: Heterogeneous systems management
EGI Service Information Management Service “GOCDB”, https://goc.egi.eu/
Globally federated compute and storage
‘hourglass’ model service specifications yet unlike TCP, the neck is thick compute service, file staging, storage, monitoring, brokering, information system, cataloging, authorization data, online-nearline-offline stage transitions, …
Service and system variety
Fabric management: Quattor

## Slide 19: Nikhef Data Processing Facility – phased deployment model
CTB
Software beta versions
Assessment and suitability
ITB
Pre-production validation
Mirror of production system at N+1
PRD
Production system
Configuration exclusively through version management
One-off installations permitted
Configuration debugging permitted

## Slide 20: HTC Computing Platform ‘Grid’ configuration
Uses Quattor configuration management suite
Federated management: modular tool-kit for installation, configuration, and state management
Shared configuration and specialisation: Quattor encourages re-use of configuration information across nodes (and across installation in a federated multi-domain service)
Inherent coherency: based on site model used to manage range of different resources, such as real machines, virtual machines and cloud resources, and ensures configuration compliance (any install always revert to its intended state)
www.quattor.org

## Slide 21: Configuration workflow for systems
Graphics: Childs et al., Devolved Management of Distributed Infrastructures 22nd Large Installation System Administration Conference

## Slide 22: LHCOPN and global data transfers

## Slide 23: ATLAS transfers to Nikhef & NL-T1
source: http://dashb-atlas-ddm.cern.ch/ddm2

## Slide 24: LHC OPN – policy based private net
www.cern.ch/lhcopn
Aim: offload T0-T1 data transfers over protected links
Plugs into the ‘ScienceDMZ’ concept – separating the ‘elephant flows’
bypassing stateful firewalls if any
Restricted policy: allow only T0-T1-T1 traffic
Scalable model using (primarily) VRF technology
RS-LHCOPN today holds 38 prefixes
~5% of total traffic to NL we are ~4.5% of the CERN membership

## Slide 25: LHCone – dynamic networking
towards full SDN capability: the L3VPN service for LHC
NSI
OpenFlow
TRILL/SPB
VRF

## Slide 26: Science DMZs – separating network flows
image and concept courtesy: Eli Dart, Brian Tierney et al, ESnet

## Slide 27: Connecting Science through Lambdas

## Slide 28: Nikhef and the world at the moment
Showing production links only – Netherlight, MSPs, and testbed not shown

## Slide 29: Building a high throughput ‘data processor’ … without breaking the bank …

## Slide 30: Interconnecting compute & storage
‘data shall not be a bottleneck’
5500 cores process together ~ 16 GByte/s of data sustained or ~ 10 GByte/jobslot/hr
are ‘bursty’ when many tasks start together
and in parallel we have to serve the world

## Slide 31: IO performance means network
100-400 TByte storage nodes now standard
Processing is done on ‘new’ data, spread over the last ~1 PiB of storage so ~ 5 storage blocks serve > 16GB/s
Realistic: up to ~ 3.2 GiB/s per node, so: ask 12 MiB/s/TiB
It also means at least 40 Gbps NICs in each box
And >> 160 Gbps sustained interconnect between all

## Slide 32: Dilemma
Tristan Suerink
Nikhef Amsterdam
PDP & Grid
32
4 rekenclusters met totaal 50x10Gb/s
4 opslagclusters met totaal 40x10Gb/s
Voldoende bandbreedte ertussen
Gescheiden routing engines verplicht
Hoe dit op te lossen?
slides courtesy Tristan Suerink

## Slide 33: Optie #1: Bouw een boom
Tristan Suerink
Nikhef Amsterdam
PDP & Grid
33
Voordelen:
  Makkelijk ontwerp
  Makkelijk uit te breiden
Nadelen:
  Duurder in onderhoud
  Veel poorten onbruikbaar
  single point of failure
slides courtesy Tristan Suerink

## Slide 34: Traditional OPN implementation

## Slide 35: Optie #2: De monoliet
Tristan Suerink
Nikhef Amsterdam
PDP & Grid
35
Voordelen:
  1 switch chassis
Nadelen
  Hoge aanschaf prijs
  Heel veel features die niet nodig zijn
slides courtesy Tristan Suerink

## Slide 36: Storage/Workernode netwerk – our choice
Tristan Suerink
Nikhef Amsterdam
PDP & Grid
36
imagery courtesy Tristan Suerink
real-time re-programming of switches to follow connected topology: “DIY SDN” using switch-native python capability
In-switch reprogramming to support LHCOPN policy based routes

## Slide 37: Grid netwerk
Tristan Suerink
Nikhef Amsterdam
PDP & Grid
37
Voordelen:
  Meer bandbreedte
  Alle capaciteit in gebruik
  Redundante opstelling naar rekenclusters
  OSPF+ECMP
  Flexibel functionaliteiten uitbreiden
Nadeel
  Grote uitbreidingen (veel meer poorten) zijn complex

## Slide 39: Deel en HEF
T Suerink
Nikhef Amsterdam
PDP & Grid
Van los en fysiek naar gezamelijk en virtueel
Juniper EX9214
Genaamd Parkwachter
Gekocht samen met AMOLF en CWI
2 x 32 x 10Gbit aansluitingen
39
slides courtesy Tristan Suerink

## Slide 40: 100Gbit
T Suerink
Nikhef Amsterdam
PDP & Grid
100Gbit testen met UvA
1e onderzoeksinstituut op Surfnet
NIKHEF-SARA koppeling
40
slides courtesy Tristan Suerink
Nikhef → SURFnet → RUG-CIT||UvA

## Slide 41: 100Gbit
T Suerink
Nikhef Amsterdam
PDP & Grid
100Gbit testen samen met UvA
1e onderzoeksinstituut op Surfnet
NIKHEF-SARA koppeling
Zeer gevoelig voor vuiligheid
Gereed voor LHC opstart
Achterliggend netwerk moet nog verder opgeschaald worden
41
slides courtesy Tristan Suerink

## Slide 42: Towards a scalable high-throughput infrastructure and platform service

## Slide 43: NDPF systems distribution

## Slide 44: Incentives for cloudification
attract more HTC use cases beyond WLCG these communities prefer different OS and software suites … although they still like a platform service!
dynamic scaling between DNI nodes, ex-DNI nodes, and ‘Stoomboot’ computing to allow short-term bursting
easier multi-core scheduling at >95% ocupancy

## Slide 45: Requirements
high-bandwidth interconnect between CPU-disk >240Gbps
true multi-tenant security & isolation
near-native node IO performance for disk and network (say, no les than 95%) at ~400 MByte/s and 10Gbps
public and on-demand (elastic) IPv4+v6 connectivity
keep dynamicity in the system (resource sharing)
permit cross-site transparent cloud bursting
hide infrastructure differences and latency where possible between SARA, RUG, Nikhef

## Slide 46: Plans for network
Network: use host-local network endpoints and distributed packets translation
  Packet copying is a major bottleneck in performance (NAT is not a sustainable solution due to overhead)
  Scalable per-tenant networking (beyond ~4000 tenants) using MPLS-EVPN and SDN integrated in the hypervisor & cloud stack
  Central termination of tenant networks in a single dedicated box (which will need MPLS-EPVN support on multiple 100G+ links)
Leave room for some 100G or DWDM to interconnect at L2 (with MPLS?) to e.g. RUG & SARA over a light path
  Tenant should see a single cluster – the network extended at L2 –quite contrary to e.g. the EGI Federated Cloud). Cloud bursting across the e-Infra will then be truly seamless

## Slide 50: Contrail Networking – DC to WAN
Source: http://www.juniper.net/assets/us/en/local/pdf/datasheets/1000521-en.pdf

## Slide 51: L2 cloud bursting: connecting services with MSPs and WDM
Extending the MPLS fabric across SURFnet MSPs, Netherlight, or Alien Waves
Graphic: SURFnet 7 DWM, SURFnet

## Slide 52: ‘NiKloud’ – a DNI service in coordination with SURF
Hybride cluster, opslag en netwerk omgeving
IP Fabric
Overlay op basis van VXLAN/MPLS
10/25Gbit aansluiting per rekennode
40/50Gbit aansluiting per opslagnode
meerdere 100Gbit per cluster; en multi-Tbit/s basisnetwerk
Hardware offloading d.m.v. DPDK op de rekennodes
‘Helicopter’ aansturing via OpenContrail (NFV)
Stricte isolatie van tenants - maar onbeperkte connectivity
‘Gebruiker krijgt de macht’

## Slide 53: (More) Discussion Time!