## Slide 1: Building scalable e-Infrastructures for research
David Groep, Nikhef
November 10, 2020
Physics-DKE colloquium
Making hardware, software, and people collaborate

## Slide 2
Scaling & the ‘data deluge’ … with data comes processing
Data from various sources, for public entities: data ca. 2018, indicative, within ~ factor 2
LHC volumes: LCG Resource Scrutiny Group & CERN; 2020 SKA and LOFAR volumes: ASTRON/Michiel van Haarlem, 2020
imagery: Powers of Ten, Eames Office LLC (available at www.eamesoffice.com)
Notes: Data deluge
Data hides treasures that unlock mysteries of our Universe Computing is essential to find them!
by investing NOW in the FuSE effort we are able to
afford compuing 2025 onwards – the proposal states that this is “upfront”
investment to save having to do brute-force, expensive computing in the late 2020s
we cannot afford to put a gap
how much data are we talking about?
Relative volumes. What is hidden here is that the associated computing for these roadmap infrastructures is quite a bit more complex than at Google and Facebook.

## Slide 3
Data is distributed – but collaboratively interpreted
3
Haarlemse Chemische Kring
protons
Atlas
ATLAS
ALICE
LHCb
Pierre Auger - cosmic rays
Gravitational Waves
SKA-Low (impression, to-be-built in .za)

## Slide 4
Nikhef PDP - an overview
4
>170 institutes in >42 countries and economic regions
Computing ~ 1,000,000 cores
On-line disks > 310 PB
Archival > 390 PB

## Slide 5
source: Andrea Sciaba et al. for the WLCG Resource Evolution WG, CHEP2019

## Slide 6
Dutch-only (!) compute requirements for LHC, KM3NeT, and SKA, until 2030
Scaling across all science domains
Source: FuSE, the Fundamental Sciences E-infrastructure, 2019
https://fuse-infra.nl/
Even then, it will be sufficient if and only if
GPU and parallelism are fully exploited
throughput per core continues to increase
data access patterns will match system design
100Mcore-hrs/yr = 11400 cores at 100% occupancy

## Slide 7
Infrastructure: dealing with data processing at scale
2: collating compute, storage, and networks
building ‘facilities’
peering and global networks
stressing networks
research ‘cloud’ services
3: accessing services, collaboratively & securely
community building in a multi-national federation
global trust and identity
securing the infrastructure of an open science cloud
our National e-Infrastructure
1: matching algorithms and systems design
designing for high-performance processors
rethinking design patterns for work & data orchestration
systems - systems
people - systems
people - people

## Slide 8
Atlas image source: Simone Campana for WLCG, 135th LHCC Meeting Open Session, September 2018
“It’s just hardware”
performance goes up, doesn’t it?
processor performance
memory bandwidth and on-die caching
accelerators (GPU, &c)
wider and faster PCI bus throughput
faster storage and global interconnects
… but …

## Slide 9
What we knew was coming …
Helge Meinhard, Bernd Panzer-Steindel, Technology Evolution, https://indico.cern.ch/event/555063/contributions/2285842/
Figure left: Herb Sutter, Dr.Dobbs Journal 2004, updated 2009, see http://www.gotw.ca/publications/concurrency-ddj.htm
CERN Computer Centre (T0 + lxbatch)
projection of different scenarios at start of HL-LHC

## Slide 10
Yet exploiting even these improvements need people …
… and implementations that take ‘hardware’ into account
Graph: measured HS06 and registered SpecINT06 Rate (base) performance per core, with SMT disabled, for the Nikhef Data Processing Facility NDPF (HTC compute) line is not mononotically increasing because of other design choices (power efficiency) and price-performance optimisation chosen
Application performance (“HEPSPEC06”) diverging from system capability (“SpecINT”)
2007 Core 2 efficiency: Sverre Jarp, CHEP 2007 (!)
SPEC benchmark: spec.org, «Rate Base» (R/B) measures throughput under full load of all cores
AMD Naples
AMD Rome

## Slide 11
AMD “Naples to Rome” – boost in application (“HS06”) performance due to new memory (I/O) architecture and direct access to all memory banks
And of course depends on hardware & CPU architecture
Image by AMD
retrieved from https://www.nextplatform.com/2018/11/06/amds-long-road-from-naples-to-milan-centers-on-rome/

## Slide 12
And why some changes will not impact performance at all
Image source: AMD, retrieved from https://m.hexus.net/tech/news/cpu/135479-amd-shares-details-zen-3-zen-4-architectures/

## Slide 13
Common element: moving data is ‘expensive’, so
‘keep on computing as long as you can, and don’t move data around’
e.g. AMD (and for others: single-socket systems), are better since there are no (useless) cache coherency delays and improved direct memory access
similarly, keep your GPU busy … as data comes from (slow) RAM
Bigger is Better - if you keep it together
Image sources: NVidia ‘Massively Parallel Computing with CUDA’
Getting to be a quite specialised field – use frameworks to implement key code … or just ask Daniel Campora et al.

## Slide 14
and if it doesn’t quite fit …
SuperMicro (branded as ‘Lambda Blade’)
4U chassis, supporting 10 consumer-grade GPUs …
… with a bump
Image source: https://lambdalabs.com/products/blade

## Slide 15
Luckily, many things in this world are conveniently parallel
HEP events & simulation
ligand matching
structural biochemistry
…
Beyond the single box
challenge is not in the parallelism itself, but in global compute with data
just like difference between SI06 and HS06 showed data as the driving factor
Image: Nikhef D0 farm in 2001

## Slide 16
shared multi-community infrastructure
Already EGI e-infra has >250 communities just doing HTC
Conveniently parallel: a global infrastructure for research
Right-hand graphic: EGI operations portal, https://operations-portal.egi.eu/vo/

## Slide 17
Nikhef Data Processing Facility – multi-community service
NDPF voview short 1 October 2018
LHC ATLAS
LHCb
LHC Alice
Grav.Waves
Dark matter Xenon1T
Life Sciences, MinE, WeNMR
‘just one of these sites’
NDPF HTC platform
member of a federated service with SURFsara, Nikhef, RUG-CIT
high-throughput storage at SURFsara and Nikhef,
long-term storage at SURFsara,
interconnected by SURFnet, and authentication by TCS and IGTF

## Slide 18
Getting the data to process … in the right place
Rucio FTS image: “The ESCAPE Datalake” Aris Fkiaras, CERN, February 26th, 2020 ESCAPE WP2 eDIOS
https://indico.in2p3.fr/event/20203/sessions/12778/#20200226
DIRAC image from: A. Tsaregorodtsev, CPPM IN2P3, EGI Webinar, 7 June 2016 https://indico.egi.eu/event/2978
ESCAPE reference components: Rucio, FTS, and DIRAC

## Slide 19
Storage as infrastructure – even a few PBytes requires some organization
management challenge is #files, not capacity
cost challenge is throughput, not capacity
Nikhef storage infrastructure
‘making disks collaborate’
for the management software, see https://dcache.org
alternatives exist, like DPM https://lcgdm.web.cern.ch/dpm

## Slide 20
Data distribution for WLCG
source: https://monit-grafana.cern.ch/d/000000420/fts-transfers-30-day
2.6M

## Slide 21
pre-staging all data locally supports latency hiding, posix-style access with lseek(2), ‘$TMPDIR’
e.g. why there are Data Transfer Nodes (DTNs) in the ‘Science DMZ’ concept
Structuring of frameworks impacts systems design
Photo HGST nVME from: Dmitry Nosachev on Wikimedia Commons CC-BY-SA
Image Science DMZ and Data Transfer Nodes: ESnet fasterdata.es.net
but, recently, pre-staging starts coming at a cost, when using SSDs as local data ‘scratch’ area … because of their unique element: ‘endurance’

## Slide 22
Frequency distribution observed on the NDPF execution nodes for outside (‘grid’) access (blue) and local access (orange)
Access pattern is rather different. But why?
external users pre-stage, because that is built into the frameworks (like DIRAC, Athena), where local users can use streaming access (‘dCache NFSv4’) yet there are changes in pre-stage streaming behaviour over time
different types of workload: ntuple-data analysis vs (re)processing
…
WORN storage – Write Once Read Never
Data: NDPF execution nodes, based on SSD SMART data, integrated over total device lifetime plot shows number of local analysis nodes scaled to DNI-WLCG count; collected using smartctl on 2020-10-28

## Slide 23
Data comes from somewhere, and has to go somewhere …
Farm (all links) data transfer to (blue) and from (green) execution nodes
NDPF cricket data deelqfx, 2020-10-28

## Slide 24
LHC Open Network Environment

## Slide 25
Evolving the physical network view
Left: IBR-LAN (1996) in H1.40;
Right: Nikhef peering visualisation (medio 2020)

## Slide 26
ballenbak.nikhef.nl
Image: Tristan Suerink
400 Gbps and 593 Mpps – now re-connected to CERN
1.02 Bpps

## Slide 27
Our science data looks akin to a DoS
evaluating resilience to cyberattack – in a cooperative way

## Slide 28
Segmentation: a network of ‘private domain’ clouds within
open-core research network model implements the enclave structure
protects against overload by no stateful components in the network path
and allows open research federated cloud using eVPN overlays
although you’ll always have some (reputational) risks even if you advertise the block as ‘customer network devices’

## Slide 29
Nikhef cloud – targeting high-throughput use cases
‘MPLSoUDP-eVPN’ using Tungsten Fabric
no NAT overhead – use public IP for external traffic
same 40/100G substrate network
direct access to storage network

## Slide 30
Image source: Free Software Foundation Europe - https://fsfe.org/

## Slide 31
Nobody wants a cloud … you want a solution! research community overlays and ‘virtual clusters’
at scale: container computing, yet with curated application images – slateci.io
NDPF Jupyter Hub experiment in our on-prem cloud
a federated infrastructure

## Slide 32
Photo by Pop & Zebra on Unsplash
on-prem cloud, or research cloud, is oft better
very cost-efficient if utilised at capacity
effective as it can provide more than ‘IaaS’
can leverage our own R&E federated access
Cross-organisation infrastructure we need an ‘ecosystem’ more than a cloud
EOSC – the European Open Science Cloud more an ecosystem (or ‘web of data’) than a ‘cloud’
and not all ‘cloud’ is what you think it is …

## Slide 33
sources: https://www.eoscsecretariat.eu/eosc-symposium-programme

## Slide 34
An ecosystem built on federated infrastructures
EOSC Portal (https://www.eosc-portal.eu/) – as built by EOSChub

## Slide 35
Whence we came: the long road to federated access
Shibboleth IdP image: SWITCH (CH)
separated authentication and authorisation, splitting identity sources, community membership, and services
Federated (R&E) AAI, the global IGTF PKI, VOMS, and ‘AARC BPA’ AAI architecture all have this as fundamental property
VO Management System VOMS attributes certificates
SAML2.0 auth flow
From disparate systems in ~2000

## Slide 36
Login via the Nikhef service proxy to gitlab, ifosim.org, …
Federated Access
https://wayf.nikhef.nl/
https://gitlab.nikhef.nl/
https://logbooks.ifosim.org/
ifosim federated AAI integration implementation
performed by Mischa Sallé
“Where are you from”
discovery screen showing entities from
the eduGAIN global interfederation

## Slide 37
Challenges of scaling federation
‘n x m’
IdP
Home Institute
SP
Collaborative
Resource
or SIte
Beyond ‘enterprise’ services, it becomes challenging!
Collaborations - by design - have their services distributed and
not that many collaborations are a legal entity
or not ‘legally authoritative’ for constituent services
or run into risk-averse, or slow, ‘home organisations’

## Slide 38
Scaling community and institutional trust
eduGAIN (global R&E) Entity Categories
Curated grouping of entities
‘REFEDS R&S’ this is a research service
‘DP CoCo’ abides by GDPR
‘Sirtfi’
cares for security response
slower adoption process
adding identity assurance needs action at all 60+ Feds & 4k+ IdPs
Use of proxy bridging components
Identity and access ‘proxy’ harmonised eduGAIN IdPs
based on entity categories
leverage Sirtfi and ‘R&S’
proxying is bi-directional
responsibility on the proxy operator
e-Infrastructure IGTF Authentication Profiles
Common baseline and profiles co-defined by relying parties
user-centric ID harmonisation with unique global naming
‘BIRCH’ real person with real name
‘DOGWOOD’ persistent linkable identifier
research-specific user base
https://wiki.geant.org/display/AARC/Current+Status+of+SAML+Entity+Categories+Adoption
https://www.rcauth.eu/ https://aarc-community.org/

## Slide 39
Research-friendly federation: REFEDS R&S … or SRAM
https://refeds.org/SIRTFI
https://refeds.org/assurance
https://refeds.org/category/research-and-scholarship
https://wiki.surfnet.nl/display/SRAM/
‘a science collaboration zone’

## Slide 40
GEANT Trusted Certificate Service
Bridges and Token Translation Services
TCS (today: Sectigo) acts as SAML Service provider to eduGAIN: eligible authenticated users can obtain client certificate for access and delegation to services
https://ca.dutchgrid.nl/tcs/
https://cert-manager.com/customer/surfnet/idp/clientgeant https://www.geant.org/Services/Trust_identity_and_security/Pages/TCS.aspx

## Slide 41
Interoperable Global Trust Federation IGTF
www.igtf.net
3 regional chapters: EMEA, Americas, AP
~ 90 Identity Providers (some leveraging a R&E federation)
~ 10 international major relying parties
~ 60 countries / economic areas / extra-territorial orgs
> 1000 relying service provider collaborations

## Slide 42
Managing complexities of distributed identity sources
ELIXIR reference architecture Mikael Linden et al.
WebFTS prototype ‘FIM4R’ in wLCG Romain Wartel et al.
communities had either invented their own ‘proxy’ model to abstract complexity
or they were composed of many services each of which had to manage federation complexity
Community images: Romain Wartel, CERN; Mikael Linden, CSC; Lukas Hammerle, SWITCH

## Slide 43
… user and group ID same across services
… minimize discovery ‘wayf’ & info screens
‘Community First’ AARC Blueprint Architecture: the Proxy
https://aarc-community.org/architecture/
AARC BPA 2019
https://aarc-community.org/guidelines/

## Slide 44
Interconnecting communities and infrastructures
https://aarc-community.org/about/aegis/

## Slide 45
AARC BPA’s ‘community-first’ model does not cover all EOSC cases, e.g. infrastructures acting as providers and suppliers and as attribute authority
Linking the providers and users together - AAI
EOSC AAI Federation
National Federation A
National Federation Y
National Federation Z
...
turn EOSC entities into a federation itself, linked to eduGAIN, preventing ‘user loops’ & meeting common (security) baseline

## Slide 46
Now what have we built?!
We have federation and single sign-on … … but can we share security information when needed? … timely and confidentially, protecting everyone’s reputation?
full of valuable resources (data, network, services)
Left: eduGAIN interfederation extent
Logos right: e-Infrastructures and ESFRIs
Center graphic: AARC collaboration
all I need is one account

## Slide 47
Assessing risk … in a collaborative infra
InfoSec risk assessment framework for (EOSC) services based on WISE SCI
this spider diagram is fictional – based on a idea by Urpo Kaila, CSC
https://wise-community.org/
e.g. ISO27001 can help structure or identify gaps in your knowledge, but ISO27002 should not be blindly applied without considering the federated interactions

## Slide 48
Containment & segmentation
matching the ‘open core’ research network community data & systems 1st class citizens
beeld: stichting vesting Bourtange
BC/DR
Haarlem
impression Nikhef network-level segmentation

## Slide 49
A question of when, not if
Communication:
Endpoints valid?
Form/Content OK ?
Containment
Ban ”malicious” users
Find/Stop malicious processes
Find submission IP
Forensics
Basic Forensics on binary
Network traffic

## Slide 50
A federated community security challenge
Can we coordinate our collective R&E response?
‘challenges’ based on the Sirtfi contact model
parties involved in response challenge
Report-outs see https://wiki.geant.org/display/AARC/Sirtfi+Communications+Challenges%2C+AARC2-TNA3.1
Security Incident Response Trust Framework for Federated Identity

## Slide 51
Sharing threat intel – working with our community
WLCG SOC WG
Research SOC (US)
AARC I-051 Guide to federated incident response https://aarc-community.org/guidelines/aarc-i051/

## Slide 52
Nikhef SOC – NDPF traffic analysis
NikhefSOC/NDPF ELK setup: Jouke Roorda
many ‘false warnings’: needs tuning

## Slide 53
e-Infrastructures: EGI, EUDAT, GEANT, PRACE, … and DNI!
imagery: EGI.eu
+

## Slide 54
‘DNI coordinated by SURF’
https://servicedesk.surfsara.nl/jira/plugins/servlet/desk/portal/1
Coordinated Dutch National e-Infrastructure
Single application portal (at SURF and NWO)
Resources allocated at most-suitable partners
Federated management and common innovation

## Slide 55
Connecting resources – people – organisations – data
https://www.nwo.nl/onderzoek-en-resultaten/programmas/Rekentijd+nationale+computersystemen

## Slide 56
Balanced infrastructure - based on our joint science cases
FuSE – Fundamental Sciences E-infra an integrated infrastructure for algorithms, hardware, networking, and collaboration
https://www.fuse-infra.nl/
Notes: Slide visualizes the Dutch FuSE proposal in context of the European and global activities in computing and data handling of large
infrastructures. ASTRON and Nikhef have been involved in e-infrastructure for more than 20 years.
Blue color: the general scientific European e-Infrastructures developments, mainly policy and coordination, not specific to any domain
Green color: EU and global developments that have been made closer to the experiments. Escape unifies all of them
Orange: the netherlands e-Infrastructure (hardware + expertise) funding (BiG Grid contained 20% Support and Development) and LHC roadmap.
FuSE: fits in right in the middle:
LHC roadmap has stopped in 2019
SKA and KM3NeT are new infrastrtuctures
Algorithmic developments and the access mechanisms are right in the middle of all this.
(WLCG does not dictate how ATLAS organises the data).
Story: Involvement of Nikhef and ASTRON in e-infrastructures goes back 20 years: on this slide, EU-DataGrid (below left) started in 2001. Also think of ICT @ ASTRON and Nikhef 3rd WWW site.
Already in the 90s.
The Netherlands is unique in the world in that the majority of the large scale scientific computing activies are coordinated by national policy through SURF.
This can be traced back to the BiG Grid proposal in which both Nikhef and ASTRON (LOFAR) participated.
After the LHC roadmap funding has stopped, and the upcoming SKA and KM3NeT
infra’s: a gap in national computing appears that FuSE will fit in.
note: both AENEAS and ESCAPE are bigger than FuSE
Note: FuSE is needed in the context of ESCAPE like WLCG was needed in the framework of EGEE
Below repeats much of above .. can consolidate.
Nikhef and ASTRON are key players both at the national and global scale.
Leading European projects (like AENEAS), establishing the infrastructure (like
EGI), and initiating national efforts such as BiG Grid (in which the WLCG
Tier-1 and LOFAR were key science communities) The expertise spans all key
areas of the FuSE proposal, and the strong alignment of Nikhef and ASTRON is
clearly evident also on the European level (with joint participation in AENEAS
and ESCAPE).
Big GRID is more than LHC and LOFAR
ASTERICS: eerder in traject, radio astronomy and astroparticle physics
AENEAS: design study for regional centres for SKA
hardware infrastructure deel van DNI gecoordineerd door SURF (unique in world)
- combi met data analyse op Nikhef en ASTRON + universiteiten

## Slide 57
… since some things are fun, but not quite that scalable …
Liquid CO2 cooling test bench, 24.33% overclocked using CineBench R20 best sustained, i.e. without LN2…
In a Nikhef-AMD collaboration
T Suerink, K de Roo: https://hwbot.org/submission/4539341_nikhef_cinebench___r20_with_benchmate_ryzen_threadripper_3970x_20022_pts

## Slide 58: Let It All Collaborate!

## Slide 59: A global operational infrastructure
Global distribution of computing and data placement
WLCG and EGI Advanced Computing for Research
Notes: What you see is a live movie (last saturday) of the existing network for distribution of data and compute jobs.
Shown in the movie are the Tier-1 data links to transfer the data from CERN to the 13 main processing centres, and links from Amsterdam to the closely associates analysis centres in WLCG, predominantly for the Atlas collaboration.
Dotted lines represent ongoing data transfers in real time (on Saturday Feb 8th, 2020), both over the special T1-links as well as to opportunistic processing capabity nearby (over the LHC Open Network Environment).
The coloured lines indicate job distribution from the workload management systems for WLCG. The coordination of much of the processing is done at the experiment level from CERN. Such jobs then retrieve data on-demand from the central sites.
The Dutch e-Infrastructure plays a central role in global data intensive sciences. The Netherlands – through SURF, the national institutes, and their university partners, is a global data hub, providing network connectivity, massive data storage, and compute capabilities to process the data.
The Netherlight hub transfers the bulk of the LHC data and is posed to play a similar role for the SKA. Network routes from South Africa arrive at the Amsterdam Science Park, and both SURF and Nikhef have direct peerings to receive SKA-Mid data. Data coming from SKA-Low in Australia similarly flow through Amsterdam.
The WLCG networks similarly link data in the Netherlands and Geneva, with AMS providing the hub for transfers to places like Canada, Moscow, and Taipei.
The ESCAPE project, joint bertween WLCG, KM3NeT and SKA, extends this concept through ‘data lakes’ ,where persistent storage is combined with opportunistic placement at smaller centres elsewhere.

## Slide 60
Computing on data: up to 40 million per second
Display of a proton-proton collision event recorded by ATLAS on 3 June 2015, with the first LHC stable beams at a collision energy of 13 TeV
~ 10 seconds to compute a single event at LHC’s ATLAS (as example) for ‘jets’ containing ~30 colllisions
Event processing time: v19.0.1.1 as per Jovan Mitrevski and 2015 J. Phys.: Conf. Ser. 664 072034 (CHEP2015)
filtering brings it down to ~1kHz and 1.5MByte/event
= ~ 1.5GByte/s of only ‘raw’ data
and computing post-2021 takes longer 

## Slide 61
Example from Xenon1T
https://www.science.purdue.edu/xenon1t/

## Slide 62
CPU architecture matching IO load – here: IBM PowerPC
‘Hot’ data tier at ~ 5 PiB, ‘warm’ tier of ~ 1.6PiB
12 MiB/s/TiB - about 4 PiB configured (DNI/NL-T1 plus local analysis)
‘hooikanon’: 240 (4x60) spindles, 12 TByte disks, 4x100Gbps network
4x IBM SL922 Power9 PPC servers, 8x NetApp E5700 controllers, 4 trays
‘speed through parallelism’

## Slide 63
For raw capacity, we added ‘sudder’ storage and introduced tiered (hierarchical) storage
comes in ‘units’ of ~ 1.6PByte a piece out of which we can allot shares to customers
investment is ~40% cheaper
most data is only used once, but nobody cleans up
this is especially true for the local analysis cluster
Speed vs. capacity in storage towards tiered storage
“sukade” (riblab/bieflap) 13 RU providing 1644 TByte net capacity (DR 8-10+1)
it has a 100Gbps network, but controller IO limits it to only ~3GByte/s in total
image: Nikhef H234bC40

## Slide 64
tiered storage entails some coordination
Tigran (HSM-in-dCache) at the Storage pre-GDB https://indico.cern.ch/event/578974/
Fast
dCache STBC today
Grid storage
Bulk
‘/data’
dCache bulk tier
Controlled
NL-T1 tape tiers
SURF Data Repository

## Slide 65
Yet still have their high-throughput applications
Communities moving to the cloud

## Slide 66
Reading data ‘scattered’ in a file - simply using POSIX-like IO - when done over the network severely exposes latency
and TCP slow-start makes that even worse
Scaling data access – ‘system-aware design’ at the framework layer
base graphic: Philippe Canal “Root I/O: the fast and the furious”, CHEP2010
Access pattern reflects Root versions < 5.28, before Ttree caching and ‘baskets’
Image of TCP slow-start and packet loss impact (in Mpps): Antony Antony et al., Nikhef, for DataTAG, 2003(!)

## Slide 67
‘ScienceDMZ’
Multi-pronged role
network isolation
security zoning
‘latency hiding’
caching
Image and ‘ScienceDMZ’ promulgated by ESnet (see fasterdata.es.net)

## Slide 68
14-06-2019: 1 billion pps i.e. 1 Gpps (and 522Gbps)
Our world record: 1 billion packets per sec
https://wiki.nikhef.nl/grid/1Bpps_Machine
Image: Tristan Suerink
Notes: Je kan in 4 seconden het hele ipv4 internet op de deur kloppen (pingen).
Een stoomboot node kan 10 Miljoen pakketten per seconde halen.
Een laptop kan 1 Miljoen pakketten per seconde halen.

## Slide 69
… you want a science network with a ‘back-office enclave’
Although for a research org …
‘open-core’ research network model implements enclave structure and protects against overload by having no stateful components in the network path

## Slide 70
But long-distance fat networks work fine for ‘big files’
bandwidth x delay hampers remote random access
which is why ESCAPE develops data lake caching
Some data is inherently ‘small’ and packetized
‘telemetry’ data
remote distributed event processing
but sending many packets is far more challenging on network ASIC design – so let’s test it!
Small packets – big trouble? 1.2 Bpps system
Graphic Data Lake, Simone Campana, ESCAPE WP2 DIOS
Image 1Bpps machine by Tristan 

## Slide 71
Impression of elasticity comes through overprovisioning of resources
… and thus at a cost for the ecosystem as a whole … ‘the best cloud is both full and empty at the same time’
when utilised, on-prem cloud is factors cheaper than a public one
… and works a lot better
‘Cloud’ Works because of scale

## Slide 72
Our IT is just as connected as our researchers

## Slide 73
Just ‘Identity assurance’ components are already complex

## Slide 74
Authentication & authorization – distributed access control

## Slide 75
Authentication & authorization – distributed access control

## Slide 76
The Intricate Paths of Federated Authentication

## Slide 77
AARC BPA – coherency by proxying
https://aarc-community.org/architecture/

## Slide 78: Service-centric policies – key elements to our ‘PDK’
the Policy Development Kit
https://aarc-project.eu/policies/policy-development-kit/ https://aarc-community.org/policies/snctfi/
graphic IdP-SP bridge: Lukas Hammerle and Ann Harding, SWITCH
Trust and Security for Research Collaboration in the EOSC era

## Slide 79
Collaborating e-Infrastructures
https://wise-community.org/
WISE working groups
Risk assessment methodology
Policy mapping interoperability
Common baseline AUP
Coordinated testing

## Slide 80
Proxy Membership Management service
pre-provisioning of account
access rights linked to groups and roles
At Nikhef COmanage
ssh via ldap
OpenStack
…
and VOMS
unix, batch, web portals
Provisioning proxy: SSH & OpenStack
co-development with the AARC project

## Slide 81
Evolution of the Blueprint Architecture
“Community-first” BPA approach
institutional eduGAIN, social, or community sign-in via their Research Community AAI
  community-specific services connected to a single ‘Community AAI’
  generic services (e.g. RCauth.eu Online CA) connected to >1 ‘Community AAI’
  e-Infra services connected to a single ‘e-infra SP’ proxy service gateway, e.g. EGI Check-In, GEANT eduTEAMS, Indigo IAM, EUDAT B2ACCESS, …
https://aarc-community.org/guidelines/aarc-g045/

## Slide 82
OpenID Connect Federation:
multilateral trust beyond GAFA
Beyond SAML: OIDC Fed – trust is technology agnostic
Roland Hedberg, et al., with Mischa Sallé, Jouke Roorda, Nikhef
see: openid.net → Specs & Dev info