## Slide 1: LHCb
Mission: To search for new particles and interactions that affect the observed matter-antimatter asymmetry in the Universe, by making precision measurements of B-meson decays.

## Slide 2: LHCb – Physics Observations
B0 → K+ p-
B0 → K- p+
Matter and antimatter
behave differently
2) Forbidden decay found

## Slide 3: LHCb Physics

## Slide 4: Vertex Detector
4

## Slide 5: Velo – Vacuum Vessel

## Slide 6: Velo Sensors

## Slide 7: Velo Electronics – PileUp Detector

## Slide 8: Velo Electronics – VeloPix
5.0mm
VeloPix Detector ( MediPix)
  Matrix: 256 x 256 pixels
  Pixel size: 55 by 55 μm
  Data: 12 Gbits/s per chip
Detectors very close to beam
  5.5 mm (!)

## Slide 9: Velo Mechanics – Vacuum Enclosure
Vacuum enclosure
  shield sensors from beam
  ~< 300 micron foil
Tight mechanical tolerances during venting and pump-down
Milling & welding technology

## Slide 10: Velo Mechanics- Vacuum Enclosure
RF-box:
crucial for physics

## Slide 11: Velo – Module Construction
Module construction
CO2 cooling capillaries

## Slide 12: Scintillating Fiber detector
Novel detector with scintillating fibers
  250 mm diameter
Modules with fiber “mats”
  6 meter long modules
  <100 mm precision

## Slide 13: SciFi Module End: SiPM Cooling
Read-out:
SiPM photo-detectors
To prevent radiation damage: operate at -40o C
Thermal cooling simulations

## Slide 14: Contacts with dutch industry
Support Structures:
Amstel Engineering BV, Amsterdam
Van Halteren Metaal BV , Bunschoten
Module frames:
Beltman Mechanisering BV, Hengelo
Alignment jigs and panel supports:
DutchAero BV, Eindhoven
Mechanics parts:
Jeveka BV, Amsterdam,
Rimas Technology Group, Beringe,
Hamel Metaal, Almere,
Metalo BV, Zaandam
Clean-room infrastructure:
ClimaTech BV, Nijkerk
PCB Design and asembly:
QPI Group, Helmond
Neways Electronics International, Eindhoven
Connectors and components:
ELPROMA Electronics BV, Nijendal
Cooling system:
Hoefnagel en Meijn BV, Zaandam
Swagelok Nederalnd BV
Wagenaar Koeltechniek, Zwaagdijk
Vacuum:
LouwersHanique, Hapert
RF-Box Milling:
VDL
RF-Box Welding:
Thalens PPS, Drouwenermond
Not yet specified:
Pick-and place machine
Cooling test system
VeloPix Bump bonding
Chip submission (IBM)
Vertex Detector
Scintillating Fiber Tracker
GPU programming framework
Esaote Benelux, Maastricht
Trigger