## Slide 1: The MROD
The Read Out Driver for the ATLAS MDT Muon Precision Chambers
Marcello Barisonzi, Henk Boterenbrood, Rutger van der Eijk, Peter Jansweijer, Gerard Kieft, Jos Vermeulen
NIKHEF, Amsterdam
Adriaan König, Charles Timmermans, Thei Wijnen
NIKHEF and Univ. of Nijmegen, Nijmegen

## Slide 2: Contents
• System Overview
• MROD Functionality
• MROD-1 Prototype
• Performance Study
• The next step (MROD-2)

## Slide 3
ATLAS MDT Muon Detector
~ 300.000 Drift Tubes
1172 MDT Chambers
192 -towers of 5-8 Chambers

## Slide 4: System Overview
5 – 8 chambers
MROD
160 MBytes/s
S-Link to ROB
24 ch. TDC
CSM
18 x
Chamber
Tower
CSM-Link
CSM-Link
(GOL)
(GOL)*
24 ch. TDC
24 ch. TDC
CSM
18 x
24 ch. TDC
*) http://proj-gol.web.cern.ch/proj-gol

## Slide 5: CSM Functionality
Serial to Parallel
&
Clock Domain Separator
40 Mbit/s
Data/Clock
from TDC
18 x
Serial to Parallel
&
Clock Domain Separator
40 Mbit/s
Data/Clock
from TDC
Separator
(GOL)
1 Gbit/s
1 Start bit
32 Data bits
1 Parity bit
2 Stop bits
36 bits @ 25 ns = 900 ns
1 Separator word (S)
18 TDC data words
19 words in 900 ns  85 MB/s
S
1
18
CSM

## Slide 6: MROD Functionality
TDC0, word 1
TDC2, word 4
TDC3, word 2
TDC0, word 1
TDC1, word 3
TDC2, word 5
TDC3, word 3
TDC3, word 0
TDC2, word 0
TDC1, word 0
TDC1, word 1
TDC1, word 2
TDC2, word 1
TDC2, word 2
TDC2, word 3
TDC3, word 1
Compiles the original TDC data from the CSM data stream, builds event fragments end sends these to the Read Out Buffer.
(tdc 1) 000…000
Separator word
Separator word
Separator word
Skip (do not store)
Check (do not store)
time
(tdc 0) 000…000
TDC0, word 0

## Slide 7: Summary of MROD Functionality
The MROD receives data from all of the 5 thru 8 MDT chambers which form one  tower, from their respective CSMs via Gigabit Optical Links (GOL).
The MROD demultiplexes the TDC data from the CSMs, it builds the event fragments and it sends them to the Read Out Buffers (ROB) via an S-Link optical connection.
The max. estimated throughput at a 100 kHz level-1 trigger rate and at the full LHC design luminosity is 0.8-1.4 Gbit/s.
(for details see the presentation by Charles Timmermans)
The MROD recognizes errors and exceptions in its input data streams and -- if appropriate -- informs the DCS.

## Slide 8: MROD Form Factor
1 MROD serves all (5 to 8) chambers of one  tower.
9 U VME64x board (single slot), 8 (or 6) CSMs in, 1 S-Link out.
• 1 MROD Crate (Sub rack) contains:
12 MRODs (12  Segments)
1 Crate Master with Ethernet Interface (DetDAQ)
1 TIM: TTCrx Interface Module (incl. ROD Busy)
@ 192 towers: 192/12 = 16 MROD Crates (1 per  Sector)

## Slide 9: MROD Crate
DET-DAQ
MROD
MROD
… total ...
12 x
CSMs
CSMs
TIM (TTCrx Interface)
ROD Busy
ROB
ROB
DAQ / DCS
VME64x-bus
One MROD Crate services 12 towers (one full  sector).
In total 16 crates will be required for all MDT chambers.
From TTC system
“TIM-bus”
Network

## Slide 10: MROD-1 prototype (1)
The MROD-1 is conceived as the first full size, full speed MROD prototype, with 6 input channels (extendable to 8 input channels).
MROD-1 is built around a number of Analog Devices ADSP21160 “SHARC” DSPs.
This DSP has 6 half-duplex 40/80 Mbyte/s SHARC-links. Data transfers take place under DMA control.
The MROD-1 design relies heavily on the use of these SHARC-links.

## Slide 11: MROD-1 prototype (2)
Modular design with three dual-input sections (MROD-ins) and one output section (MROD-out).
MROD-ins are daughter boards on MROD-out.
Main non-DSP components of the MROD-1 are FPGAs (and memories)
(for details see the presentation by Peter Jansweijer)
During normal operation (i.e. in the absence of errors) the FPGAs (and memories) guarantee the speedy operation of the MROD-1.
The DSPs take care of errors and exceptions.

## Slide 12: MROD-1 Prototype

## Slide 13: MROD-out Board

## Slide 14: MROD-in Board

## Slide 15: MROD-1 in H8 (2003)
Installed MROD equipment:
  1 9U VME64x crate with special P3 back plane for TTCrx Interface Module (TIM).
  2 MROD-1s.
  1 Crate Controller Processor (Linux).
  1 TTCrx Interface Module (TIM).

## Slide 16: MROD-1 crate in H8 (2003)
DET-DAQ
TIM (TTCrx Interface)
ROD Busy
ROS
MROD
6 CSMs
DAQ
VME-bus
From TTC system
“TIM-bus”
Network
ROS
MROD
6 CSMs

## Slide 17: MROD-1 in H8 (start-up)
Quite a few errors (bugs) had to be corrected in the software of the SHARC DSPs. Most bugs were related to the internal MROD-1 buffer management.
Some problems with bad connections.
Emergency implementation of MROD-Busy signal was needed due to the unexpectedly low speed of the H8 read out system (the ROS).
Only one (!) single error was found in the FPGA code (firmware) of the MROD-1.

## Slide 19: MROD-1 in H8 (summary)
MROD-1 start-up saw various problems, some of which were due to bugs and bad connections in the MROD-1 itself, some due to the down stream system.
After some weeks of painstakingly testing and debugging, the MROD-1 eventually ran stably and millions of events have been collected on a routine basis with a typical rate of 1 kHz.

## Slide 20: MROD-1 performance
The MROD-1 throughput (data and trigger rates) could not be tested in H8 due to limitations of the set-up.
A program to assess the MROD-1 has been launched at NIKHEF:
CSM output data is externally emulated in software or can be generated by dedicated CSM-like hardware. The simulated data is injected in the MROD-1 via optical links. This effort is ongoing and is intimately related to the optimization of the SHARC software.
For details and the latest results see the presentation by Jos Vermeulen.

## Slide 21: MROD-1 Implementation Choices
Use of Gigabit Optical Link (GOL): One-way optical connection which nicely the matches the required bandwidth (19*40 Mbit/s).
Extensive use of SHARC DSPs: MROD-1 relies heavily on SHARC-links for internal data-transfer. Moreover SHARC offers easy adaptability, flexibility and testability. FPGA does not have to deal with errors and exception conditions.
Application of TTC Interface Module (TIM) by UCL.

## Slide 22: The next MROD (MROD-2)
The MROD-2 will be fully integrated, i.e. it will consist of one single PCB VME64x module, without any daughter boards (except for the S-Link output). This eliminates a large number of connectors and thus reduces cost and enhances reliability.
The GOL receiver logic will be integrated in the MROD-in FPGAs.
The MROD-2 will have 4 MROD-ins (hence 8 inputs).
The next MROD may use a next generation DSP, the TigerSHARC.