## Slide 1
MROD-1 software
Testing
TigerSHARC in stead of the 21160?

## Slide 2
MRODin event fragment
with header sent to
MRODout via SHARC link
Input
Manager1
process()
MRODin software structure (data flow)
LinkDMA
Controller
Event
Info
Buffer1
Event
Buffer
Manager1
process()
process()
inform(…)
release()
next(…)
release()
push(…)
next(…)
release()
checkEventArrived()
setupEventDMA(…)
checkEventSent(…)
event length & id 1
event data 1
Event
Data
Buffer1
128k
Input
Manager2
Event
Info
Buffer2
Event
Buffer
Manager2
process()
inform(…)
release()
next(…)
release()
push(…)
next(…)
release()
checkEventArrived()
event length & id 2
event data 2
Event
Data
Buffer2
128k
process()
OutputManager
Separate data streams from 2 FPGAs via SHARC external bus
Chained
DMA
Blocks represent
C++ objects
Endless
DMA
Endless
DMA

## Slide 3
while (running)
{
theInputManager1.process();
theEventBuffermanager1.process();
theInputManager2.process();
theEventBuffermanager2.process();
theOutputManager.process();
theControlManager.process();
}
During normal running and for two active inputs this loop is executed:
Interrupts signal fault conditions only and do not occur during
regular operation.
The Control Manager takes care of communication with a controller
(via the MRODout) and of controlling state changes
NB: "process" methods are "inline" methods

## Slide 4
Event data may be overwritten if
the buffer is not emptied fast enough.
This can happen in case of an XOFF
on the ROL or for many large events
arriving directly after each other.
When the available buffer size in the
EventDataBuffer drops below a certain
limit an error flag is raised and events
need to be skipped (the latter is not yet
implemented). Halting the transfer of
event data from the FPGA to the SHARC
appears at first sight attractive, as there
may be more buffer space available
in the ZBT RAM. However, recovering
from an overflow in the ZBT RAM is not
possible by skipping events in a controlled
way, as is possible for preventing
overflow in the buffer in the SHARC.
(NB: in the MROD-1 it is not possible
to halt the transfer of event data from
the FPGA to the SHARC temporarily).
Input
Manager1
process()
Event
Info
Buffer1
Event
Buffer
Manager1
process()
inform(…)
release()
next(…)
release()
push(…)
next(…)
release()
checkEventArrived()
event length & id 1
event data 1
Event
Data
Buffer1
128k
Endless
DMA

## Slide 5
Length and
event id
information 1
Event
data 1
Input
Manager1
Event
Data
Buffer1
56k
Event
Data
Buffer4
56k
Length and
event id
information 4
Event
data 4
Input
Manager4
OutputManager
Event fragment with
header sent to ROL
GivePointerToFreeSpace
( spaceRequired)
process()
process()
process()
EventAvailable(streamId)
GetPointerToEvent()
ReleaseEvent()
ReleaseEvent()
EventAvailable(streamId)
DMA
DMA
MRODOut software structure (data flow)
..............
Blocks represent
C++ objects
GivePointerToFreeSpace
( spaceRequired)
GetPointerToEvent()
Via one SHARC link
Via one SHARC link
ROLDMA
Controller
SetUpDMA()
GetEventSent()
Chained
DMA, at max.
256 words per chain
4 x

## Slide 6
while (running)
{
theInputManager1.process();
theInputManager2.process();
theInputManager3.process();
theOutputManager.process();
theControlManager.process();
}
During normal running and for three active inputs a loop similar
to the main loop of the MRODin is executed:
Interrupts signal fault conditions only and do not occur during
regular operation.
The Control Manager takes care of communication with the crate
controller and of controlling state changes

## Slide 7
Length and
event id
information 1
Event
data 1
Input
Manager1
Event
Data
Buffer1
56k
GivePointerToFreeSpace
( spaceRequired)
EventAvailable(streamId)
GetPointerToEvent()
ReleaseEvent()
DMA
Via one SHARClink
A DMA for transfer of event
data is only started when
enough space in the buffer is
present (14.4 kByte is needed
for at max. 100 words per TDC
and 18 TDCs per CSM).
Transfers across a SHARC
link are subject to handshaking
-> event data cannot be
overwritten.
Optimization is possible here
with the help of fixed size
DMA transfers or endless DMA
and retrieval of the length and
event id information from the
buffer.

## Slide 8
MRODout: at max. 256 words can be transferred as one
block to the S-link, as the FIFO in the S-link interface has a
size of 256 words. A write attempt to a full FIFO will result in
a stall of the external bus until there is place again in
the FIFO. There is a flag signalling that the FIFO is empty.
-> On the basis of this flag blocks of at max. 256 words
can be safely transferred.
Under normal conditions the data leave the FIFO with the
same speed (160 MByte/s) as they enter the FIFO. However,
an XOFF on the ROL will cause the FIFO to fill (this caused
problems last summer in the H8 testbeam, as a resulting bus hang
prevents communication between the crate controller and
the MRODout and may result in a VME-bus error).

## Slide 9
Operational aspects
The SHARCs are booted via the VME-bus, the MRODout SHARCs
directly via their internal memory, the MRODin SHARCs via their
links. All can, after booting, communicate with a server program
running on the crate controller, which provides support for terminal
and file I/O. These facilities cannot be used for high rate data-taking,
but are very useful for debugging and for error reporting.
Program development
The Visual DSP++ environment running under Windows is needed for
cross-compiling and linking and producing loadable files. Program
testing in an environment simulating SHARC and FPGA specific
features has proven to be very useful for initial program development
and debugging and for bug hunting. This is done under
MACOS X or Windows with the Metrowerks Codewarrior IDE
exploiting its debugging and code navigation features.

## Slide 10
Status software
Working on transition to C++ on the basis of the software
used in the H8 testbeam. This results in improved
maintainability of the software, while optimization of the
performance is no longer hampered by the lack of information
hiding in the software written in C.
Performance
"H8 software", single channel input, output to S-link:
about 70 kHz max. event rate
C++ software, 6 channels, output to S-link, extrapolated: 72 kHz

## Slide 11
One MRODin, one input channel, MRODout acting as data-sink,
two words per TDC: 130 kHz
One MRODin, two input channels, MRODout acting as data-sink,
empty events (only headers and trailers): 75 kHz
One MRODin, one input channel, MRODout with S-link output,
empty events (only headers and trailers): > 104 kHz (event rate
limted by generator)
Two MRODins, one input channel, MRODout with S-link output,
empty events (only headers and trailers): 87 kHz
Three MRODins, one input channel, MRODout with S-link output,
empty events (only headers and trailers): 72 kHz (1 output SHARC)
MRODout program clearly can be optimized (e.g. chained DMA
for output not yet implemented), further optimization of MRODin
program also seems to be possible
(very recent result indicates
95 kHz to be possible)

## Slide 12
2. Testing
With programmable data generators in laboratory,
HW/SW functionality, including error handling / speed
2. In simulated environment: for debugging software.
With cosmic-ray setup: "real-life" testing with full
DAQ chain, setup to be used for MDT testing,
planned start: 1 February 2004
H8, 2003 and in combined testbeam 2004

## Slide 13
Several programmable data generators are available:
MRODout with appropriate software, with fixed data pattern
an event rate up to 130 kHz is possible with correct parity bits,
"CSMUX", FPGA based, fragment size per TDC Poisson distributed,
1 of each 256 fragments artificial large to simulate noise,
very high frequency possible, driven by pulse generator,
>> 100 kHz event rates possible. Three generators are
available, more can be constructed. Errors can be introduced
in the data (not in the present version),
SHaSlink (PCI card with prevous generation Sharc) based,
same software as for MRODout is used, but lower rates (~ 75 kHz).
Rate can be increased if parity bits can be ignored. Five
SHaSlink cards are available and can be synchronized to each other
and to an MRODout functioning as data generator.

## Slide 14
Many possibilities for testing under a variety of conditions,
which are being exploited.
NB: the data generated by the software generators tends
to be very bursty, which can be helpful to find problems
which may not show up when testing with identical time
intervals between successive events.
Additionally:
the cosmic ray setup (5 chambers) can be used
as high-rate data generator by lowering thresholds and
triggering at random,
for testing the MRODout the MRODins can be used
in emulation mode.

## Slide 15
Overview of results obtained so far with "CSMUX" for
max. rate (in kHz) for Poisson distributed event size (average
4 words per TDC), truncated at the values indicated). For
larger truncation values the bandwidth of 40 MByte/s of the
link between MRODin and MRODout limits the event rate.

## Slide 16
The processing resources of the SHARC DSPs used may
be sufficient for sustaining event rates up to 100 kHz,
but not much headroom is left (if any) for other tasks.
Analog Devices has introduced the TigerSHARC as successor to
the current SHARC series. A second generation TigerSHARC,
the ADSP-TS20x series, is becoming available. These processors
have clock frequencies of 500 / 600 MHz instead of the 80 MHz
used for the SHARCs in the MROD-1. In addition a number of
improvements have been made in the architecture and functionality
of the device compared to the ADSP-21160 used in the MROD-1.
Also the TigerSHARC has communication links (4 or 2) like the
21160, an MROD-2 design based on the TigerSharc could
therefore be similar to the MROD-1 design.
3. TigerSHARCs in stead of the 21160?

## Slide 17
TS201, TS202, TS203
 | 21160 | TigerSHARC
Internal memory | 512 kByte | 3, 1.5 or .5 MByte
Links | 6 half duplex | 4 or 2 full duplex
Max. link speed (1 direction) | 100 MByte/s (practice: 40 MByte/s) | 500 MByte/s
Link technology | 4 bits parallel with handshaking, single-ended | 4 LVDS pairs per direction, with hand-shaking and optional error detection (8-bit checksum per 16 Bytes)
Internal memory blocks | 2, dual-ported SRAM, 64-bit wide (1 port connected via crossbar to 2 64-bit data busses, other port to peripheral bus) | 6, DRAM, 128-bit wide (connected via crossbar to 4 128-bit data busses)
Link booting | only via link 4 | via any link
DMA from/to link to/from external bus? | No | Yes

## Slide 18
Possible caveat: internal pipelines in TigerSHARC longer
(10 cycle instruction pipeline) than in 21160, could result
in smaller gain in performance than suggested by difference
in clock frequencies.
Timing for and behavior of TigerSHARC external bus differs
from that of 21160 bus, links are different (signalling at
500 MHz is non-trivial). Getting all details right in an
TigerSHARC based MROD-2 design may prove to be time-
consuming.
Furthermore the experience with the 21160 has shown that
first versions of processors and development software may
be buggy and also that Analog Devices can be slow with
delivery of relatively bug-free processors. The TS-20x series
is just coming on the market ("sampling"), and NIKHEF is only
a small customer for Analog Devices ....

## Slide 19
We ordered a development kit with two TS-201s for
evaluation of the possible gain in performance, delivery
is expected in December.