## Slide 1: From Iron to Service, a glimpse at the Nikhef computing and Data Processing infrastructure
David Groep,
October 2024

## Slide 2
Starting with the basics …

## Slide 3
DC infrastructure: power, cooling, racks, and organisation
Left-side image: frame from a movie by Anton Mors, people replaced by … Adobe Firefly (and this was its best result )

## Slide 4
the art of infrastructure construction: beyond spaghetti

## Slide 5
Data Centre: layout and floor plans

## Slide 6
Systems physical grouping by functional & security zone

## Slide 7
Network structure design: logical and topological view segmentation: a research network with office enclaves
achtergrondbeeld: Vesting Bourtange

## Slide 8
Segmentation by access class and function
Assignments from RIPE LIRs nl-fom and SN-LIR and their subclassing in AS1104

## Slide 9
Connectivity view
AS1104 and adjacent systems in October 2024

## Slide 10
Capirca – vendor agnostic rule expression
Capirca extended for SROS by synnack (https://github.com/synnack/capirca), forked from https://github.com/google/capirca

## Slide 11
Managed systems … managed networks
Capirca ACL generation for most network vendor languages (JunOS, Cisco, &c) https://github.com/google/capirca Nokia SROS support by WilcoBH (synnack): https://github.com/synnack/capirca

## Slide 12
Networks at scale: bandwidth to compute and storage
Compute-storage-transit traffic DeelQFX aggregate (data volume as measured by harbours)

## Slide 13
Each rack comes with a couple of ‘standard’ elements
remotely monitored PDUs
temperature sensor(s)
VGA+HID+RS232 switch access
1x OOBM GigE ‘dumb’ switch
1x GigE installnet (managed)
1-2x 10/25/100G data + storage networks
Basic infrastructure: ‘every rack should have one’
Shown: H234b C06 ‘SOC’ cabinet, C08 rKVM

## Slide 14
Service clusters: ‘minimally redundant operations basis’
Nikhef H234bC08: orkestbak OEXP VM service pair. Other service clusters (GSP) are similar. FabMan and PMASec may have local-store only.
‘Typical’ node has some CPU and limited local system disk, plus:
2x 10/25G VM data net 802.3ad LACP config
2x 10/25G storage network iSCSI with 2 independent fabrics
3x 1000BASE-T install/management 1x for initial install, 2x in 802.3ad
1x OOBM IPMI & Redfish, rKVM and remote media

## Slide 15
Example: GSP ‘Koning’ en ‘Prinsjes’ (2024 edition) …
NetApp ASA C250 200TB all-flash 4x100Gbps iSCSI, 4x (Lenovo SR655 EPYC 9554P 128 logical + 30TB local ‘ephemeral’ NVME storage + 1100GiB DDR5 4800MHz)

## Slide 16
Managing the NDPF and SoLR inventory

## Slide 17
But more importantly … (re)creating and managing them
SoLR systems inventory and site definition (Ansible) and the NDPF SaltStackj

## Slide 18
Zolder: 400G access LHCOPN/LHCOne CERN link
ae10: CERN via asd001b-a96-08-6-3 – daily averages; https://cricket.nikhef.nl/ target /zolder.ipmi.nikhef.nl/ae10

## Slide 19
Physical view … QFX5130 400G switch ‘zolder’ top-up
Nikhef H234bC07 – foto’s Tristan Suerink

## Slide 20
Clusters: high throughput compute and storage service
Image: Cluster ‘Lotenfeest’ at the Nikhef NDPF, acquired March 2020. Lenovo SR655 with AMD EPYC 7702P 64-Core single-socket
Data-driven workloads (like WLCG, SKA, WeNMR) need more than ‘just’ compute:
balanced features for node throughput: CPU, storage, memory bandwidth & latency, NIC & network speed
single-socket multicore systems are fine, typical: 64-128 cores per system
network: 2x25Gbps (+ ‘out of band’ management)
memory: 8 GiB/core (so ~ 1 TiB/node)
local disk: 16TB+ NVME PCIe Gen4 x4
add GPUs depending on use case
favour inference-optimized APUs in future

## Slide 21
Balanced systems design: from global to local performance
AMD, retrieved from https://m.hexus.net/tech/news/cpu/135479-amd-shares-details-zen-3-zen-4-architectures/ and https://www.semianalysis.com/p/amd-genoa-detailed-architecture-makes
Example: AMD EPYC CPUs and their influence on systems design
!! not all ‘upgrades’ relevant to all applications (Rome>Milan hardly improved HTC throughput)

## Slide 22
More than one system: Fabric Management
Nikhef NDPF Salt & Reclass (Dennis van Dok, Andrew Pickford, Mary Hester); Quattor: https://en.wikipedia.org/wiki/Quattor); SoLR Ansible
Install server
base OS
dhcp
pxe
nfs/http
Vendor
System installer
RHEL*, Solaris,
Fedora,…
System services
AFS,LSF,SSH,accounting..
Installed software
kernel, system, applications..
CCM
Node Configuration
Manager (NCM)
RPM, PKG
nfs
http
ftp
Software Servers
packages
(RPM, PKG)
SWRep
packages
(s)CDB
Managed nodes
Install Manager
Node
(re)install
cache
SW package
Manager (SPMA)
Different modalities are fine as long as all ‘production’ systems are managed and monitored
(yet this does not apply – for a reason - to the experimental technologies platform and Nationale Speeltuin)

## Slide 23
From a bunch of systems to a service
Occupancy: NDPF (DNI allocation), early 2023; other graphics: DIRAC Interware, HTCondor (UWMadison), Jupyter notebook: Nikhef Callysto service; dCache (DESY, dCache.org)
application software and (AppTainer, docker) container images

## Slide 24
Infrastructure and services for research
driven by the strategy requirements
appropriate service levels and impact
balancing stability, innovation, and engagement
Service classes
‘enterprise’ services
research computing services (local & DNI)
experimental services
Services and service management

## Slide 25
‘If they are many, they are not principles’, so we set only four:
Institutional strategy and mission directs ICT decision making ICT decisions are assessed based on the Nikhef strategic themes
Collaboration as a core value Nikhef stands for the whole of the Dutch community in (astro)particle physics and its European and global collaborations
Shared public values and responsible technology Nikhef employs, develops, and shapes technologies that preserve autonomy, justice and humanity, that builds on our academic sovereignty and integrity
Digitalisation reflects the continuity in our research programmes With research horizons measured in decades, ICT reflect this continuity in its choice of infrastructure, services, and information management, and in its human expertise
Our Principles of Digitalisation

## Slide 26
Structuring service management with https://www.fitsm.eu/
(collaboration and federation-focused light-weight ISO20k/ITILv3 rendering)
production systems of High Throughput Compute (HTC) and on-line Storage (HTS) services
system & network components supporting provisioning of public services
pre-production and systems for service portfolio development
Scope excludes by design experimental and research systems, apart from Supplier Relationship Management and procurement
FitSM – Federated IT Service Management

## Slide 27
Single source of truth
Inventory and support contract insight
Configuration Management
  for systems management several used in parallel, which is not per-se an issue: Saltstack, Ansible
Facilitates our ISM Technical and Organisational Measures
Methodological alignment with SURF DNI
Coordinated service management

## Slide 28
And … we live in a federated global world

## Slide 29
Collaboration: an inherently-cross-domain issue ..
people photo: a small part of the CMS collaboration in 2017, Credit: CMS-PHO-PUBLIC-2017-004-3; site map: WLCG sites from Maarten Litmaath (CERN) 2021
Example from the LHC Computing infrastructure WLCG
170 sites ~50 countries & regions ~20000 users
just how many interactions ??
AuthN & AuthZ, architecture and trust should align with collaboration structures, and be outward facing: open, scalable, & multi-domain

## Slide 30
Central identity management
designed to allow innovation based on REFEDS & AARC models
‘our users are the validation’
production-quality with rapid innovation cycle
Basis for all AAI (identity & access)
OpenLDAP as core
bespoke integration suite
SimpleSAMLphp IdP and SP proxy
Support SAML, OIDC, OIDfed, and REFEDS MFA & RAF natively
IdM: ‘AARC’ & REFEDS compliant Trust & Identity AAI

## Slide 31
Research Computing Services
https://www.nikhef.nl/pdp/doc/service-portfolio

## Slide 32
Analysis cluster
https://kb.nikhef.nl/ct/

## Slide 33
Can can analyze small things in an executable Jupyter paper

## Slide 34
Including analyzing the infrastructure itself …

## Slide 35
Research Engineering support and engagement
computing courses and ‘Office Hours’ concept

## Slide 36
Although users may send some rather confused questions …

## Slide 37
Nikhef Partnership facilities
Stoomboot: ~2000 cores and ~4 PByte dCache
Callysto: JupyterHub with $home and SSO login
eduVPN: securely access Callysto and your home
Mattermost’s ‘STBC-users’ channel to talk & ask
eVA, SURFdrive, and FileSender to collaborate
Global Services
WLCG, SURF DNI, and EGI: HTC compute, CVMFS, …
Experimental services: ShareMD, Commute, …
A coherent collection of emergent services
But do read https://www.nikhef.nl/pdp/doc/experimental-services before using experimental services ... Stoomboot statistics: https://www.nikhef.nl/pdp/doc/stats/stbc-grisview-week, https://www.nikhef.nl/pdp/stats/stbc/intern/stbc_summ_plots

## Slide 38
Experimental services
https://www.nikhef.nl/pdp/doc/experimental-services

## Slide 39
Network monitoring: the SOC, MISP and WLCG SOC-WG
Nikhef SOC, H234b C06 WLCG SOC: David Crooks and Liviu Valsan, ISGC2019 proceedings, PoS(ISGC2019)010

## Slide 40
MISP Threat intel sharing (plus Shodan & ShadowServer)

## Slide 41: When things go south …
Backup and BC/DR

## Slide 42
But if something does go belly-up we should know what to do

## Slide 43
BCDR
The Nikhef XXXXXXXXXXXXXXXXXXX BCDR setup – foundational service capability more than 30km away from the primary site …