## Slide 1: AuthN Middleware Requests
compiling the wish list for authN functionality for EGI
David Groep, FOM-Nikhef and NL-NGI for EGI global task O-E-15
This work is supported by EGI-InSPIRE under NA2

## Slide 2: Why, and Why Now?
Trust anchor releases repeatedly run into ‘trouble’ in deployment
  inconsistencies in the distribution itself (1.39/1.41)
  increasing number of trust anchors
  supposedly-standard features not supported in M/W
Middleware behaviour ‘suddenly’ changes
  use of namespaces RPDNC format in VOMS/Admin implemented in 2009 appeared in production in 2011 http://indico.cern.ch/getFile.py/access?contribId=16&resId=9&materialId=slides&confId=73381
  changes are useful, but not always sufficiently-well advertised

## Slide 3: More reasons why
Operational issues
  CRL downloading and checking is not reliable
  lots of superfluous downloads
  in recent EGI ops VO incident, revocation did not take effect at some sites even after 18 hours
Future hazards
  try to prevent spreading of NSS library use in m/w since this is dangerous for scalability and stability
  re-confirm adherence to CBP’s and standards

## Slide 4: My Wish List: functionality
Support throughout all middleware for SHA-2
  starting December 2012, SHA-2 based certs may start to appear 'in the wild' without further warning…
Support for OCSP allowing for *both* use of
  AIA in the EE certificates itself, and
  for site-configured trusted responders
Support any number of CAs
Failures should be graceful
  incorrect or expired data for a single trust anchor MUST NOT affect the other trust anchors in the set

## Slide 5: Wish List: compliance
honour meaning and scope on extensions
  an attribute that says emailProtection is to protect email, not for signing documents, etc.
accept RFC3820 proxies everywhere
  and do the proper thing for proxyPathLen constraints
  beware of NSS again!
allow CRL files to be updated on a file system
  be prepared to re-read such files and implement new CRL contents at any time

## Slide 6: Wish List: don’t break it!
Support drop-in (directory based) trust anchor distributions, and continue to do so
  no monolithic databases please, no NSS on disk
Announce semantic changes to EGI/NGI&IGTF
  e.g. moving to namespaces needs prep for RPs
  document, and tell which component does what
contribute to the drafting of a new standard for an RPDNC language,
  based on the GFD.189 analysis
  participate in CAOPS

## Slide 7: Where does the wish list go?
via EGI TCB to the middleware providers with which EGI has an MoU
  EMI – harmonize the stack, and define functional unity in any Common Authentication Library
  IGE – is consistent, but needs OCSP support; and beware of NSS in moving to Fedora
discuss next week at EMI All Hands meeting

## Slide 8: Did I miss something?
Please add Real Soon, so that it can be considered by EGI