Part 3
tracking detectors
material effects
track models
fitting with momentum

---
passage of particles through matter
particles traversing through a medium interact with that medium
  - they loose energy
    - ionization: dominating effect for particles other than electrons/photons
    - bremsstrahlung: dominating effect for electrons
    - pair-production: dominating effect for photons
  - they scatter in (quasi-)elastic collisions: multiple coulomb scattering
we'll briefly discuss these two effect because
  - important for understanding how tracking detectors work
  - important ingredient to track fitting
for a real overview, look at relevant section in PDG

---
energy loss by ionization
energy loss depends on particle momentum and properties of medium
from PDG:
energy loss of muons in Cu
expressed in MeV cm2/g
in the region 1-100 GeV energy, momentum dependence is mild
mean specific energy loss described by Bethe-Bloch formula
number density of electrons
ionization energy

---
energy loss by ionization (II)
examples of typical energy loss, at 'minimum ionizing'
  - 1 meter air: 0.22 MeV
  - 0.3 mm Si: 0.12 MeV
  - 1 mm iron: 1.1 MeV
energy loss is a stochastic process, approximately described by Landau distribution
looking again at these numbers,
they cannot be correct.
your homework: calculate!
variations in energy loss can be large
in particular, there is an 'infinitely' long tail

---
radiation length
high energy electrons loose energy predominantly by bremsstrahlung
radiation length X0: mean distance over which electron looses all but 1/e of its energy by bremsstrahlung
also characteristic length for pair production: survival probability for photon is 1/e over a length 7X0/9
thickness of detector often expressed in 'fraction-of-radiation-length' x/X0
examples
  - 1 meter air: x/X0 = 0.003
  - 300 micron silicon: x/X0 = 0.003
  - 1 mm iron: x/X0 = 0.06
tracking detectors should be thin, calorimeters should be thick

---
multiple scattering
charge particle traversing a medium is deflected by many small-angle scatters, mostly due to Coulomb scattering from nuclei
scattering distribution described by theory of Molière
roughly gaussian for small angles, RMS for central 98% given by
square-root of radiation thickness
~ 1/momentum
charge of incoming particle
q
medium
particle

---
example of multiple scattering effect
take this two layer detector that measures position and angle of track
x
position resolution:  = 10 micron
distance between planes: L = 10cm
thickness of scatterer: x/X0 = 0.003 --> typical thickness of Si wafer
z
resolution on slope without scattering medium
filling in the Moliere scattering formula: q0(1GeV) = 0.7 mrad
thickness of detectors itself can degrade resolution considerably
precision of slope measurement in Si detector usually only determined by first few hits

---
tracking detectors
tracking detectors measure the position of a particle at several well-defined points along its trajectory
in most multi-purpose detectors, tracking system consist of
  - a 'vertex' detector: good position resolution close to interaction point
  - a 'spectrometer': measure momentum from curvature in magnetic field
some things to worry about when designing a tracking detector
  - impact parameter resolution (lifetimes)
  - momentum and direction resolution (invariant mass)
  - weight: multiple scattering, loss of particles due to interactions
  - radiation hardness, granularity, efficiency
the most popular tracking devices are wire drift chambers and silicon strip detectors

---
wire drift chambers
ionization of molecules along particle trajectory
electrons/ions separated by large field
electrons collected at anode sense wire
drift time is measure for distance between wire and trajectory
typical spatial resolution: 200 m
typical spacing between cells: 1cm
relatively low cost/covered surface
relatively light
sketch of a 'drift cell'
cathode wall,
usually grounded
anode wire
typically 2kV
~5mm
gas volume

---
example: LHCb drift chamber
'straw tube' chamber
cathode straws made of kapton with conductive condensate
straws combined in long (4m) modules
subset of layers rotated by +-5o

---
example: babar drift chamber
cylindrical, 'open' geometry: wires for both anodes and cathodes
field map
anode
cathodes
in the 'U” and 'V' layers, the wires are not parallel to the z-axis: stereo angles

---
silicon strip detector
measures ionization in doped silicon substrate
typical strip pitch: 50-100 m
resolution: better than pitch/sqrt(12), down to ~10 m
(make use of division of charge between strips)
relatively high cost per covered surface
relatively heavy, radiation hard

---
example: LHCb silicon strip detector
21 tracking layers
R-phi geometry: some planes measure distance to beam pipe, others measure angle phi
~1m
Interaction
region
Downstream

---
stereo views
wire chambers and silicon strip detectors measure distance of charged particle to a 'line' in space: single coordinate measurements
if all strips are parallel, can only reconstruct trajectory in 2 dimensions, namely in plane perpendicular to the strips
  - this is why most tracking devices use so-called 'stereo views'
  - strip orientations different in different planes
different scenerios for rotation angles
  - large angle, perpendicular strips
    - position resolution equal for both axis in plane
  - small angle, typically 5o:
    - measure one coordinate more accurate than the other
    - easier for track finding (tomorrow, part 5)

---
tracking detector geometry
two typical geometries
  - forward geometry (also 'forward spectrometer')
    - covers only small part of total acceptance
    - usually at fixed target, but sometimes at collider (LHCb)
  - cylindrical geometry (also 'central detector')
    - covers as much acceptance as possible
    - most detectors at colliders
important for our discussion: coordinate systems and tracking parameterizations differ for these two setups

---
central detector
not typical: Babar is asymmetric
example: Babar
B-field parallel to z-axis (~ parallel to beam)
bending plane is xy-plane
magnetic field approximately constant throughout tracker volume
drift chamber
Si strip detector
magnet
y
x

---
forward detector
straw tube tracker
example: LHCb
Si tracker
magnet
B-field along y-axis (vertical)
'bending plane' is xz-plane
magnetic field non-zero only in part of tracking volume
x
z

---
track models
track model: parameterization of charged particle trajectory
in stationary field in vacuum, motion of stable particle completely described by initial position and momentum --> 6 quantities
however, tracking detectors don't measure where particle started
  - initial position can be chosen anywhere along trajectory
  - track models have 5 parameters
if multiple scattering kinks are included in the track model, the situation becomes more complicated: many more parameters
because magnetic field configurations differ, the actual model depends on the detector geometry

---
particle trajectory in constant magnetic field
equation of motion in magnetic field
velocity is constant: coordinate along trajectory
in homogeneous field, particle trajectory follows helix with curvature radius
example: in Babar field of 1.5T
--> radius for particle with pT = 1GeV/c is 2.2m
helpful formula: electric charge in 'hybrid units'

---
helix parameterization
if field along z-axis, helix trajectory can be parameterized as
motion in
xy-plane
'poca': point of closest approach to z-axis
position and momentum along trajectory in terms of these parameters
where
of course, no need to remember this, but useful to have seen it once

---
non-homogeneous magnetic field
in real detectors magnetic field is not homogeneous
  - can still use helix parameterization, but parameters are now defined locally: they depend on coordinate along trajectory
  - changing this coordinate is called 'propagation'. we'll discuss it in more detail tomorrow
usually, the magnetic field is measured on a grid (the 'field map')
  - numerical methods are used to interpolate on the grid and to integrate the field along the trajectory
  - there is always a compromise between the accuracy of the integration and speed
  - it is a not uncommon source of momentum bias

---
parameterization in forward detectors
helix parameterization useful when detector fully embedded in approximately constant field
in forward detector like LHCb, no field in large part of tracking system
more suitable parameterization in terms of straight lines
now express coordinates as
function of z along track
using (numerical) integration
of B field between origin and z
these coordinates are again defined locally: use B field integration to express them as function of z
if field along y, 'kick' in magnetic field
for example, LHCb:  B dz = 4.2 Tm --> tx 0.13 for 10 GeV particle

---
extension of toy track fit model
momentum of
generated particle
introduce a 1 Tesla magnetic field
from now on
units are [cm]
to keep things simple, use parabolic trajectory (rather than circle)
position at z=0
slope at z=0
curvature

---
fitting with momentum
fit for position, slope and curvature
kalman fit and global fit still give identical results
note that to fit for curvature, we need at least 3 points on the track

---
momentum resolution
using what we discussed this morning, I tried to write down full expression
inverting a 3x3 matrix isn't that easy, so I cannot guarantee that it is right!
it is also not particularly illuminating, so let's try something simpler:
  - note that measurement model is still linear in all track parameters
  - therefore, resolution in curvature does not depend on curvature
in the absence of multiple scattering, the relative momentum resolution is proportional to the momentum

---
momentum resolution (II)
we can go a little bit further: curvature resolution must be
  - proportional to hit resolution
  - inversely proportional to another length-squared (dimensions ...)
translating that into the momentum, gives
think of 'BL' is the field integral: the more field on the trajectory, the more bending and therefore more momentum resolution per hit-resolution
think of the remaining 'L' the arm of the spectrometer: the longer the arm, the more precise you can measure direction, therefore curvature, therefore momentum
the full expression contains moments of z-coordinates of tracking planes